## Slide 1: Propulsion PDR
Project Manager: Cameron Flannery
Deputy Project Manager: Bill Lieu

## Slide 2: Agenda
Motor Overview
Nozzle Overview
  Dimensions
  Thermal
  Fluid Flow
Avionics Integration
  Chamber Pressure
  Camera and Antenna Mount
Section Adapter
Risks

## Slide 3: Vehicle Overview (Major Components)
6 BATES grains
Ablative Nozzle
Section Adapter
Nosecone
Propulsion
Q-Class Motor
APCP (Aluminum Fuel/Ammonium Perchlorate Oxidizer)
Ablatively cooled nozzle
BATES grains
General
2 piece aluminum airframe
Aluminum section adapter
¾ power series nosecone
Carbon fiber
Note: Fins still under design review
7’8”
17’
Avi-bay
Recovery System

## Slide 4: Motor Overview
Q-class motor
6 BATES Grains
APCP Propellant (Aluminum Fuel)

## Slide 5: Thrust
Q-motor
  Impulse range: 18,400-36,800
  Intrepid motor: 27600

## Slide 6: Nozzle Overview
Phenolic
(2-pieces)
Aluminum Retainer
Aluminum Carrier
Aluminum Skirt
Graphite Throat

## Slide 7: Dimensioning
Calculating Optimal Expansion Ratio*:
6.75”
2.30”
*equation from Rocket Propulsion Elements
** at sea-level
Ideal**: 6.894 – calculated with combustion products properties
Actual: 2.934
Under-expansion results from manufacturing capabilities
Exact impact on performance is difficult to calculate due to liquid combustion products (Al)
Performance decrease of ~5% expected

## Slide 8: Nozzle Design – Stresses
Material Properties:
Phenolic Liner: Liner thickness; ¼”
Heat Transfer Through Phenolic Liner:
Nozzle Al reaches max(T) ~ 580 K
1” of Al material thickness at hottest point
Yield Strength: 35,000 psi
Max Hoop Stress: 2,437 psi
F.S. > 14

## Slide 9: Nozzle Design – Fluid Flow
Aim:
Prevent cavitation
Prevent separation of flow
Analysis:
CFD Analysis
  Assumes gaseous combustion products
  Results in approximately 10% error due to aluminum in propellant

## Slide 10: Nozzle Design – Fluid Analysis

## Slide 11: Design for Manufacturability
6061 Series Aluminum
Phenolic and graphite relatively simple to machine
Cone Nozzle:
  Easy to machine with a lathe
  No crazy contours
Drawings created with GD&T for each part

## Slide 12: Risks & Issues
Over-expansion is not quantified
  Solution: is to perform a static fires at sea-level with different expansion ratios
Cavitation and Separation of Flow
Phenolic Thermal Barrier
  Melting point below temp of chamber
  Solution: replace phenolic with carbon at nozzle entry

## Slide 13
BACKUP SLIDES